|  | ......................... Pcs. .............................. € .............................. € GEZE Active Stop damping system fitted on the leaf for controlled dampened opening and closing of as well as keeping open swing doors on the interior. For timber doors with standard fold geometries and timber frames. With varnished covers. Damping and closing from approx. 25° door opening angle, damping and opening from approx. 60° door opening angle. Free swing between 25° and 60°, opening and closing damping forces can be adjusted via a valve even in the installed state. Maximum door opening angle 140° Door opening angle can be set variably between 80° and 140°. Barrier-free in accordance with DIN 18040-2 due to low opening forces. Max. 45 kg door leaf weight, for left and right single-action doors ( ) Set GEZE ActiveStop surface-mounted wood white RAL 9016 ( ) Set GEZE ActiveStop surface-mounted wood silver RAL 9006 ( ) Set GEZE ActiveStop surface-mounted wood similar to stainless steel ( ) Set GEZE ActiveStop surface-mounted wood according to RAL |
| --- | --- |
|  | ......................... Pcs. .............................. € .............................. € GEZE Active Stop damping system fitted on the leaf, for controlled dampened opening and closing of as well as keeping open swing doors on the interior. For glass doors with timber frames. With varnished covers. Damping and closing from approx. 25° door opening angle, damping and opening from approx. 60° door opening angle. Free swing between 25° and 60°, opening and closing damping forces can also be adjusted via a valve in the installed state. Maximum door opening angle 110° Door opening angle can be set variably between 80° and 110°. Barrier-free in accordance with DIN 18040-2 due to low opening forces. Max. 45 kg door leaf weight, for left and right single-action doors ( ) Set GEZE ActiveStop surface-mounted glass white RAL 9016 ( ) Set GEZE ActiveStop surface-mounted glass silver RAL 9006 ( ) Set GEZE ActiveStop surface-mounted glass similar to stainless steel ( ) Set GEZE ActiveStop surface-mounted glass according to RAL |