|  | ......................... pc € .............................. € .............................. Panic motor lock set GEZE IQ lock EL Self-locking panic motor lock GEZE IQ lock EL for single-leaf doors with external control tested and approved in accordance with EN 179 and EN 1125! Panic unlocking via latch or panic bar; changeover function for unlocking from outside; integrated electrical escape and child proofing to counteract misuse. Divided and separated cross latch for absolute unencumbered crossbar projection without jamming even when preloaded! Can be combined with any access control system Operating modes: night-time operation, secured by day and permanently open Secured by day operation: door opener function by means of targeted locking or release of the cross latches Night-time operation: steel bolt 20 mm bolt locking crossbar projection / motorised bolt entry less than 1 sec. Permanently open: bolt withdrawn and cross latch not locked All required contacts are integrated in the lock and provide potential-free reporting: Deadbolt contact (with 95 % crossbar projection) Latch contact (with latch activation 10°) Cylinder contact Auxiliary lock contact (door open/door leaf enclosed) Release contact (bolt completely in lock case and cross latch loose) In case of fire alarm or power cut automatic changeover to mechanical basic and panic function as well as self-locking. Prepared for installation of profile lock cylinders; with 9 mm square nut. Closed and corrosion-resistant steel lock case in DIN sizes, front metal of stainless steel; lock can be used for DIN left or right doors without conversion For use in escape and rescue routes or in fire protection doors, fittings are required in accordance with EN 179 or EN 1125:. For approved fittings, please refer to the currently valid certificate versions 0757-CPR-229-7013137-5-2 / 0757-CPR-229PANIK-7013137-4to certify the durability. Only GEZE components tested and approved together in accordance with EN 179 and EN 1125 may be installed! Please see the following EC certificates of conformity for approved fittings: 0757-BPR-229-09-003 / 0757-BPR-229-09-004 Nominal voltage: 12-24 V DC Current consumption: temporarily 250 mA at 24V; 500 mA at 12V (incl. control unit) Supplied in a set comprising: 1 pc motor mortise lock IQ lock EL with front metal plate 1 pc motor lock control MST 210 1 pc connecting cable 12-core; 10m 1 pc cable duct open 1 pc reed switch contact set ( ) IQ lock EL 9235 (distance 92 mm, backset 35 mm) ( ) IQ lock EL 9240 (distance 92 mm, backset 40 mm) ( ) IQ lock EL 9245 (distance 92 mm, backset 45 mm) ( ) IQ lock EL 7255 (distance 72 mm, backset 55 mm) ( ) IQ lock EL 7265 (distance 72 mm, backset 65 mm) ( ) IQ lock EL 7280 special backset 80 mm ( ) IQ lock EL 7210 special backset 100 mm Accessories: ( ) 1 pc. power supply 24 V DC part no. 109637 ( ) 1 pc. GEZE panic bar (EN 1125) configurable part no. 119005 To ensure all functions of the IQ lock EL a door closer is to be fixed to the door. ( ) 1 pc. TS 5000 part no. 027333 |
| --- | --- |