|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer TS 3000 V with mechanical hold-open device, with infinitely adjustable closing force size 1 – 4 in accordance with EN 1154, with guide rail, closing force can be set at the side, closing speed and latching action are front adjustable, standard installation on door leaf/hinge side Alternative to the guide rail with mechanical hold-open device: ( ) with T-Stop guide rail, with integrated opening restrictor and mechanical hold-open device. Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) acc. to RAL |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer TS 3000 V BC with mechanical hold-open device, in accordance with infinitely adjustable closing force size 1 – 4 in accordance with EN 1154, with guide rail, closing force can be set at the side, closing speed, latching action and hydraulic back check are front adjustable, standard installation on door leaf/hinge side Alternative to the guide rail with mechanical hold-open device: ( ) with T-Stop guide rail, with integrated opening restrictor and mechanical hold-open device. Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) acc. to RAL |